## Slide 1: Community Emissions Data System (CEDS)

## Slide 2: Community Emissions Data System (CEDS) - New Historical Emissions for Aerosol and Chemistry Research
PNNL-SA-112479
Steven J. Smith*, Rachel HoeSly
Joint Global Change Research Institute
College Park, MD
ssmith@pnnl.gov
Ryan M Bolt
Han Chen
Leyang Feng
Rachel Hoesly
Cecilia Moura
Patrick O'Rourke
Jonathan Seibert
Linh Vu
Yuyu Zhou
PREVIOUS
Grace Duke
Tyler Pitkanen
and the CEDS Project Team
*Also Department of Atmospheric and Oceanic Science, University of Maryland

## Slide 3: Motivation
Emissions estimates (aggregate & gridded) for aerosol (BC, OC) and aerosol precursor compounds (SO2, NOx, NH3, CH4, CO, NMVOC) are key inputs for aerosol and air pollution research and Earth System Models
    Needed for historical and future simulations, validation/comparisons with observations, historical attribution, and uncertainty quantification
The current historical dataset used by GCMs/ESMs (Lamarque et al. 2010) was a major advance in terms of consistency and completeness. This data, however, has a number of shortcomings.
    Only extends to 2000 with coarse temporal resolution (10-years)
    Time series for many of the species formed by combining different data sets leading to inconsistencies
    No comprehensive uncertainty analysis provided (available only for SO2 – Smith et al. 2011 and earlier BC/OC datasets – Bond et al. 2007)
    Underlying driver data not made available with emissions data set
    Methodology not consistent across emission species
    Process was not designed to be repeatable and easily updated

## Slide 4: Community Emissions Data System
Instead of this
Produce
Timely “research” estimates for emissions of aerosol (BC, OC) and aerosol precursor compounds (SO2, NOx, NH3, CH4, CO, NMVOC) are key inputs for aerosol research and Earth System Models
Needed for historical and future simulations, validation/comparisons with observations, historical attribution, uncertainty quantification, IAM calibration and validation, and economic/policy analysis.
X sector
X region
X sector
X fuel
X country
X state/province
Produced using an open-source data system to increase data transparency and facilitate research advancements.
Uncertainty essential for estimates of more recent years.

## Slide 5: Methodology
Approach: Hybrid of bottom-up emissions & inventory
    Develop a default dataset (GAINS emission factors, EDGAR, etc.)
    Calibrate to country-level inventories at the sectoral level where available and reliable (e.g., most policy-relevant). Similar to approach for RCP/CMIP5 data and EDGAR-HTAP.
    Most of the effort is in gathering input data
      Driver data (historical energy, agricultural output, other sectors)
      Default emissions factors. Sectoral emissions for calibration.
    Methodologies similar to Smith et al. (2011) & Klimont et al. (2013)
Produce “a” best estimate, not a fully independent estimate
    In most OECD countries much effort goes into estimating emissions, so use those. Important when control levels are changing over time.
    Emissions factors are changing less rapidly in many developing countries (but are less well known in many cases).
    Some countries (e.g. China, SE Asia) – changes are also rapid –are also more uncertain. Challenging. Wider community involvement can improve results.

## Slide 6: System Diagram

## Slide 7: Overall Project Timeline
Phase I: 2015
    Build emissions data system
    Updated dataset for CMIP6 focusing on recent decades (Fall 2015)
Phase II: 2016 – 2017
    Consistently estimate uncertainty over time and region
    Expand sub-regional detail for large countries and extend emissions estimates over entire industrial era
    Improve gridding, add seasonality and other characteristics
Implementation
    Modular, data-driven system, in the R open-source platform
    Flexible, automated system
    Consistent with country-level inventories (where desired/appropriate)
    Open source code and input data (where possible)
    Tool for emissions research more broadly
Community input and review in both phases.

## Slide 8: I. Interim CEDS Emissions Dataset for CMIP6
Interim emissions data product that updates the Lamarque et al. (2010) dataset in time for CMIP6.
      Recent emissions consistent with country inventory data over approximately ~1970 – 2014
      Early Winter 2015 Data: SO2, NOx, CO, NMVOC, NH3, CH4, BC, OC, CO2
      EDGAR 4.3 (0.1°) basis for gridding and default emissions
      Extrapolate to earlier years using RCP data (e.g. HYDE)
      Future scenario will be harmonized to depart from this starting point
      Additional features will be added in Phase II
Emission Data Used
Gains (Default EF)
US Emission Trends
Canada Emission Trends
UNFCCC Reporting
EDGAR, REAS, Adl Results Asia, US NEI, EMEP
Calculation Status (Oct 1, 2015)
Emissions of SO2 by Country, Sector, Fuel
(1960/1971 – 2014)

## Slide 9: Fire emissions
Use GFED4s for 1997-2014 and calculate for each grid cell emissions for various categories and fire frequencies
On a regional level: scale current emissions back in time using proxy data indicating emission levels (charcoal, ice core, visibility) or using changes in land use or cover with changing fire frequencies
Use DGVM’s with fire models as well as statistical fire models or assumptions to fill gaps and provide uncertainty range
Notes: So we will make for each grid cell a look-up table what emissions are for various land use or covers and for various fire frequencies. In places where we don’t have proxies we then use the land cover information and the derived emissions for this. Factors like CO2 fertilization will be based on models.

## Slide 10: Fires: Spatial and temporal resolution
GFED-era (1997-2014):
  Monthly, for 2003 onwards daily
  0.25°×0.25°
Pre-GFED era (1750-1996):
  Monthly but based on GFED climatology (so assuming no change over time)
  Annual values scaled where possible, for example when using visibility data starting from 1950 and high-resolution ice core or firn records
  For other regions or time periods decadal estimates
  1°×1°
Source categories: savanna, forest, deforestation, agricultural, peat
Species: all that are available in GFED. Others can be calculated based on emission factors

## Slide 11: Engagement
Your input is encouraged
    ssmith@pnnl.gov
    We have a web site
      http://www.globalchange.umd.edu/CEDS/
    And a listserv for updates
      Send an email to listserv@listserv.umd.edu with the email body: “subscribe cedsinfo”. (You will get a return e-mail asking you to verify your subscription.)
The data system and input data will be released as open source software
    (You will have to purchase a license for the IEA energy data.)
    Including capability of producing gridded emission datasets

## Slide 12: END