## Slide 1: Using S2D data to predict spring flood volumes in selected Swedish rivers
Kean Foster

## Slide 2: Porjus idag
<number>
Hydropower was
the driving force

## Slide 3: Background - Hydropower in Sweden
<number>
Sweden is the biggest hydropower producer in the EU and the 10th biggest worldwide (IEA 2012)
Hydroelectric capacity : 16 781 MW
  % of total installed capacity : 42.79%
  % of total renewable capacity : 67.81%
Annual production (last 10 years) : 73 TWh
  approx. 45% of the country’s total consumed electricity

## Slide 4: Hydrologic Forecasts
<number>
Short range forecasts, up to 10 days ahead
Based on a meteorological forecast
Most valuable at high flows (flood warnings), and for short term reservoir planning
Long range forecasts, 1 to 6 months ahead
Climatological forecast based on historical precipitation and temperature records
Most valuable for water resources planning and operation of reservoirs

## Slide 5
Climatological ensemble:
Historical time series
HBV
Forecast
1961, 1962, 1963, 1964, 1965, 1966, 1967, 1968, 1969, 1970, 1971, 1972, 1973, 1974, 1975, 1976, 1977, 1978, 1979, 1980, 1981, 1982, 1983, 1984, 1985, 1986, 1987, 1988, 1989, 1990, 1991, 1992, 1993, 1994, 1995, 1996, 1997, 1998, 1999, 2000, 2001, 2002, 2003, 2004, 2005, 2006, 2007, 2008, 2009, 2010, 2011…

## Slide 6: Long-range forecast, 0201 - 0731
<number>
simulated discharge (m3/s)
accumulated runoff volume
(86400 m3, DE)
Simulations made for February to July with precipitation and temperature series from many different years
A statistical analysis is made to estimate the probable runoff volume over the forecast period

## Slide 7: Long-range forecasts the importance of the initial conditions
<number>
snow water equivalent (mm)
accumulated runoff volume
(86400 m3, DE)
accumulated runoff volume
(86400 m3, DE)
Forecast made from 1989-02-01
Forecast made from 1996-02-01

## Slide 8: IHMS – Integrated Hydrological Monitoring System
<number>

## Slide 9: Climatologic ensemble: Limitations
Climatologic ensemble  Seasonal forecast evolution follows the climatology of the driving data
No notable improvement in performance over the last 25 years
Arheimer et al. 2010
Notes: 1
C:a 40-50% förbättring med ”perfekt prognos”
Upp till 20% förbättring genom förbättrad kalibrering

## Slide 10: IHMS
<number>
Licensed user interface
End-user has full control over forecasts i.e. frequency of forecasts, lead-time, model setup etc
Driving data is provided by SMHI
  End-user can use other data sources i.e. their own observations
Once a year SMHI and the end-users meet to discuss model performance.

## Slide 11: IHMS
<number>

## Slide 12: The Ångerman River
<number>
The hydropower system of the river Ångermanälven
IHMS

## Slide 13: Ongoing Research
<number>
SMHI and Lund University
Projects
  ELFORSK/HUVA - seasoanal forecast prototype
  EUPORIAS - improvements to model chain and demonstration prototype (Ångerman river)
  SPECS - test meteorological seasonal forecasts in an operational context (Ångerman River)
Aims:
  Improve forecast performance
  Reduce impact of future climates on forecast performance
  Improve how forecasts are presented

## Slide 14
Reduced ensemble:
HBV
Forecast
Historical time series
1961, 1962, 1963, 1964, 1965, 1966, 1967, 1968, 1969, 1970, 1971, 1972, 1973, 1974, 1975, 1976, 1977, 1978, 1979, 1980, 1981, 1982, 1983, 1984, 1985, 1986, 1987, 1988, 1989, 1990, 1991, 1992, 1993, 1994, 1995, 1996, 1997, 1998, 1999, 2000, 2001, 2002, 2003, 2004, 2005, 2006, 2007, 2008,2009, 2010, 2011…

## Slide 15: Reduced ensemble: TCI method
Teleconnection Climate Indices
  NAO
  AO
  SCAND
Select all years with comparable TCI combinations
Run HBV with reduced ensemble
Analogue
years
HBV
Spring flood
volume forecast
Maj-Jun-Jul
Notes: 1
C:a 40-50% förbättring med ”perfekt prognos”
Upp till 20% förbättring genom förbättrad kalibrering

## Slide 16: Reduced ensemble: CP method
Circulaion patterns
  Daily MSLP
  Fuzzy-rule based classification
Identify years with similar CP combinations (analogue years)
Run HBV with reduced ensemble
Analogue
years
HBV
Spring flood
volume forecast
Maj-Jun-Jul
Notes: 1
C:a 40-50% förbättring med ”perfekt prognos”
Upp till 20% förbättring genom förbättrad kalibrering

## Slide 17
Seasonal NWP based forecast:
HBV
Forecast
NWP
~100 km

## Slide 18: ECMWF forecasts in HBV: method
ECMWF seasonal forecasts
  51 ensemble members
  Daily P and T → Bias correction and remapping to HBV grid format
Run HBV with ECMWF ensemble
ECMWF
ensemble
P och T
HBV
Spring flood
volume forecast
Maj-Jun-Jul
Notes: 1
C:a 40-50% förbättring med ”perfekt prognos”
Upp till 20% förbättring genom förbättrad kalibrering

## Slide 19
Statistical downscaling:
Forecast
NWP
~100 km
SVD

## Slide 20: Statistical downscaling: method
Atmospheric variables predictors from NWP (ECMWF)
  Pressure field variables
  Temperature/radiation variables
  Moisture variables
Observed Seasonal dischage volumes
In December
GCM forecast
Jan-Feb-Mar
SVD
Forecast
spring flood volume May-Jun-Jul
Notes: <number>

## Slide 21: Schematic of the Multi-model prototype
Climatological ensemble
Reducerad climatological ensemble
S2D ensemble
Snow data
Weighted Multi-model
Hydrological model
Statistical model

## Slide 22
Multi-Model Forecast example:
Notes: <number>

## Slide 23
Multi-Model Forecast example:

## Slide 24: Forecast example: Initialised 1Jan
Notes: <number>

## Slide 25: Forecast example: Initialised 1Jan

## Slide 26: Forecast example: Initialised 1Apr
Notes: <number>

## Slide 27
Forecast example: Initialised 1Apr

## Slide 28
Preliminary findings

## Slide 29
Seasonal hydrological forecasting skill

## Slide 30: Preliminary findings
Climatological spring flood forecasts are difficult to beat
For single rivers and forecast dates, a reduction of the forecast error by up to 30% points are attainable by circulation pattern analysis or statistical downscaling
By a weighted multi-model, an overall reduction in forecasted error by almost 10% points are attainable
Notes: 1
C:a 40-50% förbättring med ”perfekt prognos”
Upp till 20% förbättring genom förbättrad kalibrering